VW / AUDI / SEAT / SKODA

1.Switch Ignition ON and leave the key in the ignition.
2.Mechanically lock the vehicle using the drivers door using a second key.
3.Using the remote control press the unlock button once, and the horn will sound once.
4.Wait 6 seconds and press the unlock button once to activate the coding procedure. The remote control will be programmed.

Note: When performing programming on additional remotes the procedure is the same, except you press the unlock button 2,3 or 4 times for the different remote.

For example: If programming 2 remotes press the unlock button twice with a 1 second interval between each press, repeat for 3 and 4 remotes.
5.switch ignition OFF
6.Remove key from ignition and check for operation.
7.The coding procedure can be repeated up to 4 times for additional remotes.
8.The ignition procedure can be switched OFF between programming each remote control.